## Slide 1
The recording and slides of this webinar will be made available to attendees via email later today.
PDH Certificates will be e-mailed to attendees within 2 days.
Air Compressor Component Function, Troubleshooting & Maintenance
Loran Circle, Circle Training & Consulting
Keynote Speaker
Sponsored by

## Slide 2: Q&A Format
Panelists will answer your questions during the Q&A session at the end of the Webinar.
Please post your questions in the Questions Window in your GoToWebinar interface.
Direct all questions to Compressed Air Best Practices® Magazine
Sponsored by

## Slide 3: Handouts

## Slide 4: Disclaimer
All rights are reserved. The contents of this publication may not be reproduced in whole or in part without consent of Smith Onandia Communications LLC. Smith Onandia Communications LLC does not assume and hereby disclaims any liability to any person for any loss or damage caused by errors or omissions in the material contained herein, regardless of whether such errors result from negligence, accident, or any other cause whatsoever.
All materials presented are educational. Each system is unique and must be evaluated on its own merits.

## Slide 6
Introduction by
Compressed Air Best Practices® Magazine
Air Compressor Component Function, Troubleshooting & Maintenance
Sponsored by

## Slide 7: About the Speaker
Compressed Air Systems Sales Training
Design and Consulting of Compressed Air Systems
Certified DOE AirMaster+
Sponsored by
Loran Circle
Circle Training & Consulting

## Slide 8: Five Components of an Air Compressor
Compression- Air End, rotors, stators, pistons, turbines, rotary vanes, etc.
Cooling - Coolers, air cooled, water cooled etc.
Drives - Motors, electric, diesel motors, steam driven etc.
Controls - Modulation, variable speed drives, variable capacity etc.
Electrical Systems – Power for controllers, solenoids, actuators, drives etc.

## Slide 9: Air Compressor Units

## Slide 10: Rotary Screw Air Compressor Components
The Air End of the compressor takes air in through the inlet filter under a VACUUM condition
The atmospheric air is mixed with a lubricant. This provides for cooling, sealing and lubrication
The compressed air/lubricant mixture leaves the air end and travels through the oil separator
The oil is separated and is circulated through the lubricant cooling system
The “clean” air is sent to the aftercooler for cooling to reduce moisture content. Once vapor is condensed to water, the moisture separator removes the water.
Note: If you are seeing visible moisture in your system, the issue could be the moisture separator

## Slide 11: Reciprocating Air Compressor Components
Reciprocating compressors are the simplest compressors as far as their complexity
Either loaded or unloaded
Start/Stop
They also can be multiple stages depending on discharge pressure
Very few parts
Operates on an adjustable or fixed pressure range switch

## Slide 12: Centrifugal Air Compressor Components
Air End of the compressor takes air in through the inlet filter under a VACUUM condition
The atmospheric air is started spinning and enters the impeller

## Slide 13: Centrifugal Air Compressor Components
In the first stage the air is compressed to “x” psig to start the compression to end with the desired discharge pressure. Centrifugal compressors are typically 2-4 stages, however desired discharge pressure is what determines the number of stages.
The air, after traveling through the different stages is sent to the aftercooler for cooling to reduce moisture content. Once vapor is condensed to water, the moisture separator removes the water.
*The next presentation will cover the different types of drying from the discharge of the aftercooler downstream.

## Slide 14: Coolers
Usually there are two different coolers on the compressor
One is for air
One is for lubricant
Air to Air heat exchanger (fin/fan)
Water-cooled heat exchanger (tube and shell)
Water cooled
Air Cooled

## Slide 15: Air Compressor Drive Motors
DC Series Motor
Three phase Motor
Squirrel Cage Induction Motor
Synchronous Motor
Single phase Motor
Diesel Engine
Natural Gas
Steam Engine

## Slide 16: Air Compressor Controls
Pressure Switch
Load No/Load
Inlet Modulation
Variable Displacement
Variable Speed or Variable Frequency Drive

## Slide 17: Electrical System
The electrical system provides power to the systems controls, which includes the controller, pressure switches, actuators etc.
Generally, there is a stepdown control transformer installed on the machine for voltage of various components.

## Slide 18: Troubleshooting Common Problems
Over Heating – Check with the manufacturer the amount of rise across a compressor and the temperature drop across a cooler. These will be the same
Inlet temperature of the machine doesn’t really affect the temperature of the machine
What it does effect is the temperature of the cooling air on an air-cooled machine.
With an infrared temperature gun shoot the inlet and outlet of the cooler
A plugged cooler from the outside will show a low temperature differential
What does a high temperature differential show?
Legend
Atmosphere
High Pressure Air
Oil
Oil/Air Mixture
Fluid Filter
Aftercooled Air
Thermal Valve
Discharge Air
210º
180º
190º

## Slide 19: Trouble Shooting Pressure Problems
Check your pressure with a pressure gauge at the end of the system.
A large pressure differential shows a flow restriction
Check pressure differential across filters
Check areas of distribution system for piping losses
70 PSIG
80 PSIG
120 PSIG

## Slide 20: Pressure Problems (cont’d.)
Pressure at the discharge is 90 PSIG
Pressure at the end of the line is 80 PSIG
This is an overdemand situation
The demand is exceeding the compressor capacity
There are only two reasons for pressure drop
Either flow restriction or overdemand
90 PSIG
80 PSIG
85 PSIG

## Slide 21: Maintainence
Set up a regular visual inspection program
Keep logs for equipment maintenance, temperature and pressure readings
Change your filters upon manufacturers recommendations
Use OEM parts

## Slide 22: Air Compressor Component Function, Troubleshooting & Maintenance
Thank You For Attending
Loran Circle Compressed Air Systems Consulting and Training Poland, Ohio 44514 832-906-0469

## Slide 23: About the Speaker
Technical Service Specialist, BEKO Technologies
7 years in the Compressed Air industry
Sponsored by
Jaime Munera
BEKO Technologies

## Slide 24: Compressed Air Equipment Maintenance
Tips for Compressed Air System Maintenance
Speaker: Jaime Munera

## Slide 25
Compressed Air Treatment – Products We Will Discuss For Maintenance
CLEARPOINT Filtration
RA Refrigerated Dryers
DPX Desiccant Dryers
BEKOMAT Condensate Drains
METPOINT Sensors
IMPORTANT:
Please note that the information contained in this document is general maintenance/installation guidance. Always refer to your product manual on the specific model for detailed installation, operation and maintenance information for any piece of equipment.

## Slide 26
Equipment Types
  Flanged -Threaded
Maintenance
  Filter Element
  Drain Cartridge
Maintenance Intervals
  8,000 Hours
Compressed Air Treatment - Filtration

## Slide 27
Dryer
  Drypoint RA Refrigerated
Maintenance
  Condensers Cleaning
  Drain Maintenance
  Electrical Connection Checks
  Visual Inspection
Maintenance Intervals
  8,000 Hours
Compressed Air Treatment - Refrigerated Dryers
Refrigerated Dryers – Commonly Used
38 F (3 C) Dew Point

## Slide 28
Dryer
  XCE XCP ACC
Dryer Maintenance
  Pre-/Post Filtration
  Silencers/Mufflers
  Dew Point Sensors
  Valve Service
  Safety Checks
Maintenance Intervals
  8,000 Hours
  16,000 Hours
  24,000 Hours
Compressed Air Treatment - Desiccant Dryers
Dew Points from
-4 F (-20 C) to -100 F (-73 C)

## Slide 29
Compressed Air Treatment - Zero Loss Drain
Drain Types
  BEKO 31,32 and 32 VERIO
Maintenance
  Drain Cartridge/Service Unit
  Check Connections
Maintenance Intervals
  8,000 Hours/1 Million Cycles

## Slide 30
BEKOMAT 13, 14, 16
Drain Types
  Higher volume/ Pressure units
Maintenance
  Break down, clean and Reassemble with service kit
  Check and verify connections
Maintenance Intervals
  8,000 hours/ 1Million Cycles

## Slide 31
Compressed Air Treatment – Instrumentation Sensors
FLM
Flow Meter
DPM
Dew Point Meter
SP
Pressure Meter
Sensor Types
  Flow/Pressure/Dew Point
Maintenance
  Inspection/Calibration
  Connections & Fittings
Maintenance Intervals
  Yearly

## Slide 32
Thank You!
BEKO TECHNOLOGIES, CORP. 900 Great SW Parkway SW Atlanta, GA 30336 UNITED STATES +1 (800) 235-6797 www.bekousa.com
Sales Contact Information: https://www.beko-technologies.us/en-us/contact
To Conclude

## Slide 33
Please submit any questions through the Question Window on your GoToWebinar interface, directing them to Compressed Air Best Practices Magazine. Our panelists will do their best to address your questions and will follow up with you on anything that goes unanswered during this session.
Thank you for attending!
Q&A
Air Compressor Component Function, Troubleshooting & Maintenance
Sponsored by

## Slide 34: Thank you for attending!
The recording and slides of this webinar will be made available to attendees via email later today.
PDH Certificates will be e-mailed to Attendees within 2 days.

## Slide 35
Thursday, February 17, 2022 – 2:00 PM EST
Register for free at
www.airbestpractices.com/webinars
February 2021 Webinar Compressed Air Piping System Sizing & Design
Sponsored by
Tim Dugan, P.E.
Compression Engineering Corporation
Keynote Speaker